## Slide 1: AI-Based Smart Irrigation Scheduling using BiRNN & BiLSTM
(103123022) CH. Koushik Rao
(103123124) Vrindesh Pareek
(103123066) K. Manish Kumar
CEPC22 – Hydrology & Irrigation Engineering
Department of Civil Engineering,
NIT Tiruchirappalli – 620015
Date: 10-04-2026
Presented by
Presented to
Dr. S. Saravanan
Professor, Dept. of Civil Engg

## Slide 2
INTRODUCTION
The Problem We Are Solving
🌡️ Rising Temperatures
Annual temp in Karnal rising at +0.03°C/yr causeshigher ET₀ and more water needed per crop cycle
🌧️ Erratic Rainfall
Monsoon becoming shorter but intense creating soil moisture uncertainty causing irrigation timing failure
💧 Fixed Schedules
Farmers use 50-year-old irrigation calendars leading to 30–40% water wastage or crop stress
🤖 Our Solution
AI-powered daily irrigation prediction using BiLSTM deep learning + climate change forecasting

## Slide 3
OBJECTIVES
Project Objectives
01
Compute ET₀
FAO-56 Penman-Monteith evapotranspiration for Karnal
02
Soil Moisture
Daily water balance model (FC=150mm, WP=60mm)
03
Train BiRNN
Bidirectional RNN baseline model with Bayesian tuning
04
Train BiLSTM
Bidirectional LSTM advanced model — best temporal memory
05
Compare & Select
Auto-select winner based on RMSE, MAE, NSE, R²
06
Schedule 2026–2040
Season-wise irrigation calendar for Wheat & Rice

## Slide 4
STUDY AREA & DATA
Karnal, Haryana — Study Area & NASA POWER Data
📍 Karnal, Haryana, India
Latitude: 29.6°N
Longitude: 76.9°E
Elevation: 237.6 m (MERRA-2)
Climate: Semi-arid
Soil: Loamy (Indo-Gangetic)
Max Temp: 41°C (May–Jun)
Min Temp: 7°C (Jan)
Avg Rain: ~750 mm/year
NASA POWER Variables (2011–2025)
T2M
Temperature at 2m
°C
PRECTOTCORR
Corrected Rainfall
mm/d
RH2M
Relative Humidity
%
WS2M
Wind Speed at 2m
m/s
ALLSKY_SFC_SW_DWN
Solar Radiation
MJ/m²/d
5,479 daily records | 15 Years | Zero missing values after QC

## Slide 5
METHODOLOGY
Project Methodology Pipeline
1
NASA POWER
Data (5479 days)
2
Data Cleaning
& QC
3
FAO-56
ET₀ + SMS
4
Feature Eng.
(19 features)
5
Bayesian
Hyper-Tuning
6
BiRNN vs
BiLSTM Train
7
Auto Model
Selection
8
Future Forecast
2026–2040
9
Irrigation
Schedule
10
Rabi + Kharif
Calendar
11
Output CSVs
+ Report

## Slide 6
THEORETICAL BACKGROUND
FAO-56 Penman-Monteith ET₀ & Soil Moisture Balance
ET₀ = [ 0.408·Δ·(Rn−G)+γ·(900/(T+273))·u₂·(es−ea) ] /
[ Δ + γ·(1+0.34·u₂) ]
Rn
Net radiation (MJ/m²/d)
T
Temperature (°C)
u₂
Wind speed (m/s)
es−ea
Vapour pressure deficit
Δ
Slope of sat. VP curve
γ
Psychrometric constant
Soil Moisture Balance: SMS(t) = SMS(t−1) + P(t) − ET₀(t) − IR(t) → Clipped to [WP=60mm, FC=150mm]
Irrigation Requirement:
IR = max(0, ETc − P_eff)
where ETc = Kc × ET₀
Crop Coefficients (Kc):
Wheat Rabi peak: Kc = 1.15 (Dec–Feb)
Rice Kharif peak: Kc = 1.20 (Aug–Sep)

## Slide 7
EXPLORATORY DATA ANALYSIS (EDA)

## Slide 8
THEORETICAL BACKGROUND
FAO-56 Penman-Monteith ET₀ & Soil Moisture Balance

## Slide 9
15 Year Climate Overview (2011-2025)

## Slide 10
DEEP LEARNING MODELS
BiRNN vs BiLSTM — Architecture Comparison
BiRNN — Baseline
Input: (14 time steps × 19 features)
→ Bidirectional SimpleRNN (tuned units)
→ Dropout + BatchNorm (optional)
→ Bidirectional SimpleRNN (tuned units)
→ Dropout
→ Dense(16, ReLU)
→ Dense(1) — Irrigation (mm/day)
BiLSTM — Advanced 🏆
Input: (14 time steps × 19 features)
→ Bidirectional LSTM (tuned units)
→ Dropout + BatchNorm (optional)
→ Bidirectional LSTM (tuned units)
→ Dropout
→ Dense(32, ReLU) → Dense(16, ReLU)
→ Dense(1) — Irrigation (mm/day)
VS

## Slide 11
Model Selection Based on Performance Comparison
BiRNN vs BiLSTM – Performance Metrics Comparision

## Slide 12
FUTURE FORECAST 2026–2040
Climate Change Irrigation Forecast — 2026 to 2040
Key Finding: Irrigation demand projected to increase 8–15% for Rabi (Wheat) and show higher variability for Kharif (Rice) by 2040

## Slide 13
Hystorical vs Future Monthly and Annual mean Irrigation
Climate Change Irrigation Forecast — 2026 to 2040

## Slide 14
Monthly Forecasted Irrigation Requirement (mm/month)

## Slide 15
IRRIGATION SCHEDULING
Season-Wise Irrigation Scheduling Calendar
🌾 Rabi Season — Wheat
October
Initial stage (Kc=0.30)
Skip / light irrigation
November
Germination
Every 7–10 days
December
Tillering (Kc=1.15)
Every 3–4 days ⚠️
January
Jointing–Booting
Every 3–4 days ⚠️
February
Grain filling
Every 4–5 days
March
Maturity (Kc=0.75)
Every 7 days
🌾 Kharif Season — Rice
June
Nursery–Transplant (Kc=1.05)
Daily/every 2 days ⚠️
July
Vegetative growth
Every 2–3 days
August
Tillering (Kc=1.20)
Every 2 days ⚠️
September
Heading–Flowering
Critical — monitor daily
October
Grain filling (Kc=0.80)
Every 5–7 days
November
Maturity–Harvest
Stop irrigation

## Slide 16
CLIMATE CHANGE IMPACT
Climate Change Impact on Irrigation Water Demand
Why ML Fails Here
ML models assume statistical independence of samples. Irrigation demand has temporal memory — a drought 2 weeks ago affects soil moisture today. Simple models cannot capture this.
Why BiLSTM Wins
BiLSTM gates retain cumulative climate effects. The forget gate discards irrelevant past, input gate stores new stress signals, output gate controls what influences prediction.
Rabi Impact by 2040
Temperature rise → ET₀ +3–5%
Irrigation demand +8–12%
December most critical month
Groundwater stress increases
Kharif Impact by 2040
Monsoon variability increases
Dry spell irrigation +15–20%
August–September most affected
Adaptive scheduling critical

## Slide 17
OUTPUTS
Project Deliverables & Output Files
01
Historical Dataset Processed
5,479 rows with ET₀, ETc, SMS, Irrigation, VPD
02
Model Performance Metrics
BiRNN vs BiLSTM — RMSE, MAE, R², NSE, MAPE
03
Test Set Predictions
Actual vs BiRNN vs BiLSTM — daily test period
04
Future Forecast Daily
5,479 daily predictions (2026–2040) + soil moisture
05
Rabi Irrigation Schedule
Monthly wheat schedule with advisory (2026–2040)
06
Kharif Irrigation Schedule
Monthly rice schedule with advisory (2026–2040)
07
Best Hyperparameters
Tuned HP values for BiRNN and BiLSTM models

## Slide 18: THANK YOU